## Slide 1: Project 3: Keypad and LED Patterns
Aaron Foster & Beau Coburn

## Slide 2: Overview
Create a lockable system dictated by a 4x4 keypad
Drive an RGB LED to indicate the status of the system
Drive LED patterns based on input from the keypad
Alter the speed of the LED patterns based on an input from the keypad
Switch between the patterns and return to the place where they left off

## Slide 3: Code at a Glance
Main Loop Flow Chart

## Slide 4: The Entire Picture

## Slide 5: System Architecture

## Slide 6: Pin Diagram

## Slide 7: Pseudo-Code
lock/unlock:
while(locked){
pattern LEDs off
rgb=red
call led_pattern() //Which also calls read keypad
}
while(!locked){
rgb=blue;
call read keypad
switch(case) //For A or B
if(read = 'D'){
Lock keypad
pattern iteration speed:
Switch(case){
case 'A':
increment speed by 0.25s
case 'B':
decrement speed by 0.25s
}
Overflow ISR:
toggle heartbeat every 2 overflows
set pattern flag to 1 every base_time + inc/dec
if(pattern=1){
do pattern
custom LED color
}else if(pattern=2){
do other pattern
custom LED color
}
else if(pattern=3){
do other pattern
custom LED color
}else if(pattern=4){
do other pattern
custom LED color
}
clear ISR flag

## Slide 8: A Deeper Look (The CCS variable family)
A series of variables are used to specify:
  Pattern choice
  Pattern step
  State (locked or unlocked)
  When the overflow clock is triggered

## Slide 9: Logic to Control Pattern
Stepnum
  Controlled which step the pattern was currently on
  Equivalent to pattnum1/2/3
Barflag
  Boolean that turned true when ISR was hit

## Slide 10: Keypad Development
4x4 Keypad
  All Rows and Columns connected
  Set Rows as inputs and columns as outputs
  Set one column high at a time
  Check state of rows
  If both row and column are high select input from key map
  If none are high set next column high and repeat
  This process was repeated four times to get a four digit code

## Slide 11: Patterns and Clock Development
Overflow clock was set to 0.25ms
Overflow needed to be raised by 3000 cycles to account for delaying logic in ISR

## Slide 12: Controlling and Altering Base-Time
barcounter
  Incremented each ISR call and reset when overflowing with desired time
base_time
  Varied on pattern number
  Inconsistency in instructions
switch case
  Altered time_cntl
  Prevented current time settings from turning negative and freezing program

## Slide 13: RGB Development
Using Combinations of Red, Green, and Blue several colors can be created
Red denotes the system is locked
Yellow will appear when the system is being unlocked
Blue denotes the system was successfully unlocked and ready to display patterns
Unique LED color for each pattern
Color driven by RGB_Contorl module (else if statement with each color assigned a #)

## Slide 14: Locking and Unlocking Development
Set a locked flag
Created a locked and unlocked while loop
Only scan for correct 4 digit code within while loop while locked
All other functionality will only happen when locked flag is not set
Can reset the locked flag by pressing D on the keypad

## Slide 15: End Result
System Starts Locked with LED Red
LED turns yellow when a code is entered
System unlocked and LED is blue when correct code (6969) is entered
LED patterns can be driven by pressing 0,1,2,3 which have unique LED color
Pattern will pick up where it left off when selected after another pattern
Pressing A will decrease pattern speed, B will increase speed
Pressing D will relock and reset system